## Slide 1: MAE 253 – Experimental Aerodynamics I Lab 5 – Airfoil Aerodynamics (Drag)
Shreyas Narsipur
NCSU
March 18th, 2019

## Slide 2: Outline
Lab 5 - Objective
Lab 5 – Theory
Lab 5 - Expectations

## Slide 3: Lab 5 - Objective
Breakdown of automation techniques in LabView.
Study the drag characteristics of the airfoil.

## Slide 4: Lab 5 - Theory
Drag is the parallel (to oncoming flow direction) component of the force exerted on a body due to the fluid flow.
  Cd – coefficient of lift
  D – lift force
  ρ – density of fluid
  V∞ - freestream velocity
  c – airfoil chord

## Slide 5: Lab 5 - Theory
The profile drag of the airfoil can be calculated by measuring the pressure/momentum deficit in the wake of the airfoil.
Done using the wake-rake system.
Area under the pressure deficit curve gives us the drag coefficient.
  In MATLAB, the trapz() function gives you the area under a curve.

## Slide 6: Lab 5 – Expectations
Data acquired:
  Total pressure data at different angles of attack and Reynolds numbers.
  10 readings per angle of attack.
Co-plot the pressure-deficit distributions at all angles of attack for a given Reynolds number.
Plot the Cd vs. α curve for the airfoil and compare the data to XFOIL predictions.
Constants:
  airfoil chord, c = 0.3048m
  dynamic viscosity, μair = 1.825x10-5 Pa s

## Slide 7: Lab 5 – Interim Correction to Cd Data
Due to wind tunnel restrictions, static pressure at the point of measurement was unable to recover to freestream conditions.
As an interim correction, while calculating Cd for the given angle-of-attack, only consider the positive pressure deficit area curve (as shown in red) instead of the complete area under the curve (outlined in black).
Note that this is just a fix. To get accurate Cd values, you will have to apply the pressure correction equations given in Schlichting’s ‘Boundary-Layer Theory’.