## Slide 1: MAE 253: Experimental Aero 1 Introduction to Xfoil
Pranav Hosangadi
Feb 26-28, 2019

## Slide 2: Outline
What is Xfoil?
Installation problems?
Typical analysis workflow
  NACA airfoil
  Custom airfoil
  Plotting results
Automation
Comparing with experiments

## Slide 3: Introduction
Xfoil is an open-source Fortran code written by Prof. Mark Drela and Harold Youngren
http://web.mit.edu/drela/Public/web/xfoil/
Subsonic airfoil design / analysis
Some capabilities: Inviscid, viscous analysis, airfoil design (direct and inverse)
  Create airfoil polars
  Cp distributions
  Simple BL calculations
Interactive or through a script
Good “sanity check” for experimental data
http://web.mit.edu/drela/Public/papers/xfoil_sv.pdf

## Slide 4: Installation problems?
Go to https://vcl.ncsu.edu
Create a new Windows reservation
Download xfoil for Windows, extract to C:\Users\<you>\Downloads\XFOIL6.99
Add “C:\Users\<you>\Downloads\XFOIL6.99” to path
See a TA during office hours

## Slide 5: Running Xfoil
Working directory
  Xfoil reads/writes in this directory unless you enter the full path
  cd (Win)
  pwd (UNIX)
Open command prompt / terminal, navigate to your working directory
  cd working_dir (Win & UNIX)
  xfoil
?  shows the list of commands you can give xfoil

## Slide 6: List of commands
1-4 letter commands
Some commands take arguments
  “r”: Expects a real number
  “i”: Expects an integer
  “f”: Expects a file name
  “s”: Expects a string
“.” before a command: Drill down menu
  “.” is not a part of the command
Give commands in one line or multiple lines
Commands are not case-sensitive

## Slide 7: Loading a NACA airfoil
Xfoil can generate NACA 4- or 5-digit airfoil profiles from the equations
NACA 4-digit airfoils: e.g.: NACA 0012 (symmetric) or NACA 2412 (cambered)
NACA mpT  Generates a NACA airfoil. m = maximum camber as % chord (1 digit) p = location of max. camber / chord * 10 (1 digit) T = Maximum thickness as % of chord (2 digits)

## Slide 8: Cleaning up geometry
After loading, check geometry
  sharp angles between panels
  coarse distribution of panels
PPAR: Increase number of panels, distribution of panels, etc.
  N 250
PANE: smoother airfoil if sharp angles

## Slide 9: Setting up a viscous simulation
OPER (find operating points)
  VISC 3e6 (Enable viscous mode, Re=3M)
  ITER 100 (Increase number of BL iterations)
  INIT (Initialize BL solver to alpha=0)
  PACC (Save polar to file)

## Slide 10: Finding operating points
OPER
  ALFA 5
    What’s in the output window?

## Slide 11: Finding operating points
OPER
  INIT
  ASEQ 0 25 1
  INIT
  ASEQ 0 -10 -1
  PACC

## Slide 12: Other OPER options
CPX
CPV
VPLO
DUMP
CPWR
VPAR
  XTR

## Slide 13: Viewing polars
Polar file format
pplot
  Cl vs Cd polar, drag bucket
  Cl vs alfa
  Cm vs alfa
Reading polar files in MATLAB

## Slide 14: Automating Xfoil
xfoil < script.txt
What’s in script.txt?

## Slide 15: NACA 2412 run
Let’s try again with a cambered airfoil
Create a file called script_2412.txt
Copy each xfoil command to script_2412.txt
  Including <enter>

## Slide 16: NACA 2412 run
Alpha range: -5 to 24 deg
Re = 1M
Useful commands:
  NACA, PPAR
  OPER, VISC, ITER, INIT, PACC, ASEQ
Check results in pplot

## Slide 17: Loading custom airfoils
Input format:
  x-coordinate | y-coordinate
  TE to LE US, LE to TE LS.
http://m-selig.ae.illinois.edu/ads/coord_database.html
LOAD sd7003.dat

## Slide 18: Load airfoil run
Instead of using the NACA 2412 airfoil, let’s use the sd7003 airfoil from Prof. Selig’s website.
Change the script we created for NACA 2412, create script_sd7003.dat
xfoil < script_sd7003.dat
Check results

## Slide 19: Comparing to experiment
Overpredicts
Underpredicts
Comparison of airfoil analysis techniques (XFOIL vs. RANS CFD vs. Wind Tunnel) for the DU21 A17 airfoil with a Reynolds number of 1x106
Source: Barrett, Ryan and Ning, Andrew, “Comparison of Airfoil Precomputational Analysis Methods for Optimization of Wind Turbine Blades” (2016). All Faculty Publications. 1671. https://scholarsarchive.byu.edu/facpub/1671

## Slide 20: Questions?